## Slide 1: EV4 Wiring by K. Ferhat Celik
We support you when your ideas start elevating

## Slide 2
EV40-F Layout
Temp. sensor
OPEN loop control
EV4
Uses the standard power unit
Covers up 80% of applications
YASKAWA
L1000H
EV4
EV4 Valve
Motor
Pump
Elevator controller
DOWN travel: Conventional (mechanical)
UP travel with inverter

## Slide 3
YASKAWA Drives for the EV4 system
kW size | L1000H – 400V |  | 
 | Drive Code | Line Filter | AC Reactor
3 | LC4V0007BAA-0011 | FS23639-15-07 | B 0903084
4 | LC4V0009BAA-0011 |  | 
5.5 | LC4V0015FAA-0011 | FS23639-30-07 | B 0903085
7.5 | LC4F0018BAC-9120 | FB-40025A | 
11 | LC4F0024BAC-9120 | FB-40044A | B 1103139
15 | LC4F0031BAC-9120 |  | B 1103140
18.5 | LC4F0039BAC-9120 |  | B 11030141
22 | LC4F0045BAC-9120 | FB-40060A | 
30 | LC4F0060BAC-9120 |  | B 1103142
37 | LC4F0075BAC-9120 | FB-40105A | 
45 | LC4F0091BAC-9120 |  | B 0910013
55 | LC4F0112CAC-9120 | FB-40170A | 
75 | LC4F0150CAC-9120 |  | 
L1000H – 200V drives are also available !
Voltage range of the drive should match with the mains power!
Drive selection is done according to the required current.
Example: CIMR-LC4F0039BAC-09120
4 shows that it is a 400V drive
39 indicates the nominal current available from the drive (+40% overload is possible for 45 seconds)

## Slide 4
What is received in an EV4 package?
A YASKAWA L1000H drive, which contains the hydraulic software, is delivered in the EV4 package. The package also includes a temperature converter, temperature sensor, line filter and AC reactor.
EV4 valve
L1000H Yaskawa Drive
Temperature converter & temperature sensor
Line filter
AC Reactor
EV4 User Manual
L1000H
Line filter
AC Reactor
Temp. Converter & Temp. sensor
EV4 package

## Slide 5
EV4 package content
Connection of electrical components
Temperature converter is also wired to the drive

## Slide 6
EV4 Electrical layout
Connections of temperature converter & temperature sensor (See page 15 of EV4 User Manual)
Correct connection of the temperature sensor is important. After completing wiring of the EV4 system, verify the connection by reading the temperature from the drive display unit. For that select U7-07 parameter from the monitor menu. Temperature reading is in °C. If U7-07 shows -50 or a minus temperature then the wiring must be wrong. Check the polarity of the power supply to the temperature converter.

## Slide 7
EV4
EV4
Supply power and motor connections
D C
MOTOR
Motor contactors
Mains
Place the drive either in the existing controller cabinet or in a separate cabinet together with the line filter and AC reactor. Do the mains and motor connections (See page 12 & 16 of EV4 User Manual).
YASKAWA
L1000H
Line Filter
AC Reactor

## Slide 8
UP travel signalling
S1
S4
S5
S6
+24V
SC
SP
SN
S2
S3
Up call/ Levelling Speed/ Stop
Nominal Speed
Intermediate Speed
Inspection Speed
L1000H drive
Elevator Controller
RS1
RS4
RS5
RS6
Control Board
As a default setting L1000H drive uses internal 24Vdc circuit for signalling. The terminals S1 to S8 on the drive are used for signalling. In order to provide a signal, for example to the S1 terminal, the circuit between SN and S1 should be bridged. To do that, an elevator controller may be designed to have relays (shown as RS1, RS4, RS5 and RS6 ) for each terminal. The relay circuit is provided by the elevator controller, it is not delivered in the EV4 package. When the elevator controller energizes, for example the relay RS1, the circuit switch closes and S1 signal is sent to the drive.
Meaning of the terminals
S1 terminal: S1 signal is necessary for an up travel. Without S1 signal the drive will not initiate any travel. If only S1 signal is sent to the drive, the drive travels at levelling speed. In order to perform re-levelling again only S1 signal is used.
Speed selection terminals S4, S5 and S5: These are used for speed selection. For a normal (full speed) travel S4 switch should be closed together with S1. Similarly for intermediate and inspection speeds S5 and S6 are closed respectively instead of S4. When more than one speed selection switches are closed the drive runs with the lowest selected speed.
Example: When a normal speed travel is to be done, S1 and S4 switches should be closed at the same time. By doing so elevator accelerates and reaches the normal (full) speed. As the car needs to decelerate the elevator controller removes (de-energizes RS4) the S4 signal. Then the car decelerates into the levelling speed and travels at that speed. As the S1 signal is removed (de-energizes RS1) by the controller the elevator stops. When the S1 signal is removed the elevator controller should run the motor 1 second longer (apply a motor delay) to allow soft stop. If Inspection travel is to be done, in this case the same sequence between S1 and S6 should be repeated.

## Slide 9
UP signalling of EV4 drive
Full speed travel S1+S4
Intermediate full sp travel S1+S5
Inspection speed travel S1+S6
Levelling speed travel S1
Stop
switch
Decel.
switch
Input
common
Energy to motor contactors
S4 – Speed selection signal
S1 – Up run signal
1
2
3
Stop
switch
Decel.
switch
1
2
Elevator speed
Output frequency
Travel signals
Base block signal - optional
L1000H
S1 is up travel signal, without S1 elevator will not move.
S4, S5 and S6 are speed selection signals, one of which should be used together with S1 for a travel.
Base block signal is optional. Unless base-block signal is removed by the elevator controller a run cannot occur.

## Slide 10
Verification of UP signalling
Monitor Menu, parameter U1-10: Input terminal status displayed as „0“ for no input otherwise „1“
From Monitor menu verification of correct signalling can be done.
How? Go to Monitor menu and observe the parameter U1-10.
00000000
00000001
00001001
Examples of runs
No signal received by the drive, elevator will not run
Levelling run: Only S1 signal is received
Nominal sp. run:
S1 and S4 signals are received
00100001
Inspection sp. run: S1 and S6 signals are received

## Slide 11
Down coil wiring
EV40
EV40
D C
MOTOR
Motor contactors
Mains
Connect the D and C coils to the controller outputs. If there will be an UCM/A3 valve connected to the control valve, its coil connection to the controller should also be done.
The voltage to the down coils should match with the coil voltage on the EV4 valve.
The same sequence is applied for the down travel but in this case, energy is sent to the D & C coils on the EV4 valve by the elevator controller.
For full down speed D & C coils are energized.
To decelerate into slow speed C coil is de-energized. To stop at floor energy to the D coil is removed.
YASKAWA
L1000

## Slide 12
EV4 Modernization applications